## Slide 1: Hardware Communication with I2C

## Slide 2
Introduction
Inter Integrated Circuit
developed 1982 by Philipps Semiconductor (now NXP)
no licensing since 2006
TWI (Two-Wire-Interface) bus is essentially identical
use case:
  simplicity
  low costs
nowadays maximum transfer rates up to 5 MHz possible, commonly up to 400 kHz

## Slide 3
Example Setup
SLAVE
SLAVE
MASTER
LEDARR
MOTORS

## Slide 4
Terminology
Term | Description
Master | generates clock (SCL) starts and stops communication sends commands
Slave | device that listens to the bus addressed by the master
Multi-master | more than one master can attempt to control the bus at the same time without corrupting the message
Arbitration | control-procedure on multimaster-systems ensures simultaneous access does not result in loss
Synchronization | clock-stretching
SDA | Serial Data
SCL | Serial Clock

## Slide 5
I2C-Properties
synchronous serial communication  two signals
half-duplex  alternating bidirectional operation
address-oriented (as opposed to message-oriented)
supports multimaster

## Slide 6
I2C-Properties
open-drain system (in contrast to UART and SPI)
  bus drivers can only pull SDA to LOW
  less conflicts by avoiding contradictory pulls
Pull-up resistors restore both lines always to HIGH

## Slide 7
Specification
state of SDA may only change on SCL LOW
SDA has to be stable during HIGH of SCL
one clock pulse for each data bit
START: HIGH-to-LOW on SDA while SCL is HIGH
STOP: Low-to-High on SDA while SCL is HIGH

## Slide 8
Specification
ACK: Acknowledge
receiving device is given control after first 8 bits
ACK by pulling down SDA
missing ACK terminates transmission
up to Master how to proceed
possible address space is 7 bits
MSB is transmitted first
eighth bit RW indicates data direction
RW: LOW ≙ write, HIGH ≙ read

## Slide 9
Transfer modes

## Slide 10
Summary: I2C by the numbers

## Slide 11
Pros and Cons of the different buses

## Slide 12
Sources
Content:
http://ln.iuk.fh-dortmund.de/~gebhard/STA/vortraege/I2C-Bus__Joachim.pdf
https://www.nxp.com/docs/en/user-guide/UM10204.pdf
http://i2c.info/i2c-bus-specification
https://www.i2c-bus.org/i2c-primer/clock-generation-stretching-arbitration/
https://bitwizard.nl/wiki/SPI_versus_I2C_protocols
http://www.w3service.net/vorlesungen/rechnernetze2/0010-protokolldarstellung/Grundbegriffe%20der%20Kommunikation-048.pdf
https://www.nxp.com/docs/en/application-note/AN10216.pdf
Images:
https://www.nxp.com/docs/en/user-guide/UM10204.pdf
https://www.nxp.com/docs/en/application-note/AN10216.pdf
https://www.heise.de/preisvergleich/arduino-nano-3-x-a000005-a799461.html
http://blog.pimoroni.com/introducing-the-raspberry-pi-3-b/
https://www.blinkstick.com/help/tutorials/blinkstick-pro-adafruit-neopixel-matrices
https://components101.com/motors/28byj-48-stepper-motor

## Slide 13: Thank you for your attention