## Slide 1
YOU
SEE,
TOO
useetoo.org
Lenses
Converging lenses
Diverging lenses
Thicker in the center than on the edge
Thicker on the edge than in the center
positive
convex
negative
concave
that is perpendicular to the lens plane a goes throug its central point
Parallel rays: all rays that are parallel to the optical axis will converge to a point behind the lens
Focal rays: all rays that pass through the focal point will be parallel to the optical axis after passing through the lens a
Central rays: in an approximation, the central rays will pass the lens without being refracted
Optical axis
Lens
Focal plane
Focal plane
Parallel ray
Focal ray
Central ray
Object
Image
Ray optics describes light in terms of rays – light rays are lines showing the direction of passing light.
Light ray
Lenses refract the light rays.
Parallel rays passing through a positive lens converge to a focal point behind the lens.
Parallel rays passing through a negative lens diverge as if they were coming from a virtual focal point in front of it.
Image formation with lenses

## Slide 2
useetoo.org
Positive Lenses
Focal point F‘
Focal length f‘ (positive)
Parallel rays
Optical axis
Focal plane
Lens
Object side
Image side
Positive lenses refract all rays that are parallel to the optical axis to a single point, which is called focal point.
The image is…
inverted
smaller
real
f‘
f
2×f‘
2×f
The magnifying glass, …
… , is simply a positive lens of a small focal length.
Try the lenses!
Magnification of the magnifying glass
250 mm is so called conventional near-point distance. It is given by accomodation properties of the eye.
The effect of a magnifying glass!
inverted
same size
real
inverted
larger
real
YOU
SEE,
TOO
upright
larger
virtual

## Slide 3
YOU
SEE,
TOO
useetoo.org
Negative Lenses
upright
smaller
virtual
The negative lenses refract all rays of light parallel to the optical axis in such a way that it seems like they are coming from a single point in front of the lens.
Object side
Image side
The image is always…
Try the lenses!
How does the image look like through different lenses?
f‘ = +100 mm
f‘ = +40 mm
f‘ = -50 mm
With the right lens held in the right distance, the text looks like it has the same size and orientation.
The correct text size
„Focal point“ F‘
Focal length f‘ (negative)
Parallel rays
Optical axis
Focal plane
Lens
f‘
f
2×f‘
2×f

## Slide 4
YOU
SEE,
TOO
useetoo.org
Projector
Magnification of the lens
Lens Equation
f‘
f
2×f‘
2×f
Distance s1 of the object
Distance s2 of the image
Focal length
Object height h1
Image height h2
When imaging an object through a positive lens, the position and size of the image depend on the distance s1 of the object from the lens and its focal length f'.
The image is not anywhere!
The image is not arbitrarily large!
Where is the image?
What is the magnification?
Change the distance of the lens
Exchange the lens
Lens (40 mm)
f
2×f
s1
Slide/Object
Flashlight

## Slide 5
YOU
SEE,
TOO
useetoo.org
Galileian Telescope
F‘
parallel rays
Magnification
Positive lens
Positive lens
Negative lens
The telescope is an optical instrument that magnifies objects, which are far away.
f‘Objective - f‘Eyepiece
The field of view (FOV) is
small
The image is
virtual
and upright
F‘
parallel rays
Negative lens
F‘
f‘Objective
f‘Eyepiece
Objective
Eyepiece
(100 mm)
(-50 mm)

## Slide 6
YOU
SEE,
TOO
useetoo.org
Keplerian Telescope
F‘
parallel rays
Positive lens
F‘
parallel rays
Positive lens
Magnification
F‘
f‘Objective
f‘Eyepiece
Objective
Eyepiece
(empty)
(empty)
Positive lens
Positive lens
f‘Objective + f‘Eyepiece
The field of view (FOV) is
larger than with the Galilean
telescope
The image is
virtual
and inverted
(100 mm)
(40 mm)

## Slide 7
Light microscope
YOU
SEE,
TOO
useetoo.org
The microscope is an optical instrument that makes it possible to see magnified images of objects that are too small to be seen by the naked eye.
Objective
Eyepiece
Intermediate image
Object
f‘Objective
f‘Eyepiece
Tube length
larger
inverted
real
virtual
larger
inverted
The image is…
in the intermediate image plane
through the eyepiece
F‘
f‘Tube lens
f‘Objective
Objective
Eyepiece
Object
f‘Tube lens
f‘Objective
Tube lens
f‘Eyepiece
Intermediate image
„infinite“ tube length
Old or simple microscopes use objectives that are designed for a defined tube length and they form a real intermediate image in a given distance from the objective. The intermediate image is further magnified by the eyepiece. These microscopes are „finite“ optical systems.
Newer microscopes use so-called „infinity“ optics. In this case, the objective doesn‘t form any real intermediate image. The light rays are parallel after passing through the objective. At the end of the tube, which can be arbitrarily long, is a tube lens that forms the intermediate image, which is then again
further magnified by the eyepiece.

## Slide 8
useetoo.org
Light microscope
„Infinity-corrected“ microscope
Magnification of the intermediate image
YOU
SEE,
TOO
(empty)
(empty)
Tube lens
Objective
Object
f‘Objective + f‘Eyepiece
Keplerian telescope!
Eyepiece
Objective
Object
Tube lens
Eyepiece
Intermediate image
Total magnification
(40 mm)
(40 mm)
(40 mm)
(40 mm)
(100 mm)
(100 mm)

## Slide 9
Mirror
Mirror
Smartphone
Smartphone Microscope
Object
Light Source
Camera
Objective
(empty)
Eyepiece
YOU
SEE,
TOO
useetoo.org
or
4×
20×
„Finite-corrected“ microscope
Magnification
The smartphone camera has a short focal length lens to create an image on the camera sensor. The imaging properties are therefore similar to those of the human eye.